## Slide 1: Crystals that think about how they’re growing
David Doty
Caltech
Harvard
Inria Paris
UC Davis
joint work with Damien Woods, Erik Winfree, Cameron Myhrvold, Joy Hui, Felix Zhou, Peng Yin
University of New Mexico, Computer Science Colloquium, Sept 10, 2019

## Slide 2: Acknowledgements
Damien Woods
(co-first author)
Erik Winfree
(PI)
co-authors
Cameron Myhrvold
Peng Yin
Felix Zhou
lab/science help
Ashwin Gopinath
Sungwook Woo
Constantine Evans
Jongmin Kim
Sarina Mohanty
Niranjan Srinivas
Paul Rothemund
Yannick Rondolez
Mingjie Dai
Nikhil Gopalkrishnan
Bryan Wei
Cody Geary
Deborah Fygenson
Chris Thachuk
Nadine Dabby
Joy Hui
Diverse and robust molecular algorithms using reprogrammable DNA self-assembly.
Damien Woods†, David Doty†, Cameron Myhrvold, Joy Hui, Felix Zhou, Peng Yin, Erik Winfree.
Nature 2019. †These authors contributed equally.
Caltech
Harvard
Inria Paris
UC Davis

## Slide 3
Building things by hand: use tools! Great for scale of 10±2 ×
Building things
Ljubljana Marshes Wheel. 5k years old
Newgrange, Ireland. 5.2k years old
Building tools that build things: specify target object with a computer program that then controls the manufacturing process
Mariana Ruiz Villarreal
Programming things to build themselves: for building in small wet places where our hands or tools can’t reach
Notes: 10^14 molecules in a cell. 10^14 cells in the human body.

## Slide 4: Things that build themselves
Our topic: self-assembling molecules that compute as they build themselves
I want to stick below blue & yellow and above blue & green
x10

## Slide 5: Hierarchy of abstractions
Bits: Boolean circuits compute
Tiles: Tile self-assembly implements circuits
DNA: DNA strands implement tiles
Notes: Finally, we build the tiles, out of our favorite molecule.

## Slide 6: Harmonious arrangement
0
1
1
0
1
1
1
1
1
1
0
0
1
0
1
0
1
1
1
0
1
0
1
1
1
1
1
0
1
0
1
1
1
1
0
0
a.k.a. sorting
=
=
=
=
=
=
Notes: There’s some bits… I don’t like them... Don’t care for these bits.
Now these bits on the other hand… these bits I like.
In truth, they’re the same bits, but they’re arranged so nicely, with all the 1’s on top.
How I can get the former bits to be like this?
Imagine we can examine a pair of adjacent bits and change them.
In this pair, the 0 is on top and the 1 on bottom, but we want the 1 on top, so we swap them.
This pair is already in the correct relative order, so we leave it.
These are both 1’s, so there’s only one order, so we leave it.
If we looked at these pairs again, the bits would stay the same, so we shift the reading frame; this lets more bits get swapped.
In the shifted reading frame, we have a lonesome bit on top and one on bottom, so we add half-gates to propagate these.
Now we just repeat these gates, and eventually, the bits end up sorted.

## Slide 7: Odd bits
move 1’s to here
1
0
1
0
0
1
0
1
0
1
1
0
0
1
0
0
0
0
0
0
0
1
0
0
1
2
3
6
7
5
4
1
2
3
0
0
0
1
0
0
0
0
0
1
0
0
…
6
7
5
4
1
2
3
0
0
0
1
0
0
0
0
0
1
0
0
6
7
5
4
1
2
3
a.k.a. parity
Notes: Here’s some more bits… I don’t know yet whether I like these.
I like odd numbers of 1’s, but I don’t know how many there are.
Let’s move them to this line to count them.
So the 1’s above the line should move down, but below the line they should move up,
indicating I want to allow different gates to compute different functions, so we’ll label the gates differently.
If we see two 1’s, we’ll change them both to 0.
Now, this decreases the number of 1’s by 2, so if it was odd before, it’s still odd.
Eventually the remaining 1 makes its way to the middle, and stays there.

## Slide 8: Parity
1
0
1
1
0
1
0
1
0
0
1
0
0
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
…
0
0
0
0
0
0
0
0
0
0
0
0
Notes: Now consider if we start with an even number of 1’s.
The middle two cancel, and the outer two move toward the middle.
They move again.
Eventually they meet and cancel.
And now we have all 0’s.

## Slide 9: Circuit model
i1 | i2 | o1 | o2
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
i1
o1
i2
o2
0
1
1
0
0
0
0
1
gate g: function with two input bits i1,i2
and two output bits o1,o2
gate g
g truth table
Notes: These are examples of a formal circuit model I’ll define now.
The basic unit is a gate, most gates have two input bits and two output bits, though we also allow one-input/one-output.
The gate is defined by a truth table.
The outputs can be any function of the inputs you want, so any way to fill in these output bits in the truth table defines a legitimate gate.

## Slide 10: Circuit model
i1
o1
i2
o2
gate g6,NN(i1,i2) = o1,o2 = NOT(i1),NAND(i1,i2)
Possibly different gate types on different rows within a layer
Gates organized into vertical layers consisting of many rows
3
2
4
1
5
6
7
gate g3,XA(i1,i2) = o1,o2 = XOR(i1,i2),AND(i1,i2)
i1
o1
i2
o2
one layer
7 rows in layer
Notes: Each gate has a row number, this one is row 3.
The gate connects to gates in adjacent rows.
All rows put together make a layer.
And gates in different rows can compute different functions.

## Slide 11: Circuit model
Randomization: Each row may be assigned ≥ 2 gates, with associated probabilities, e.g., Pr[g3,NN] = Pr[g3,XA] = ½
2
4
6
3
5
1
7
g3,XA
i1
o1
i2
o2
i1
o1
i2
o2
g3,NN
Notes: A feature of the model we haven’t yet seen is randomization.
The programmer can optionally specify multiple gates per row,
and assign a probability to each to be used each time the gate is evaluated.

## Slide 12: Circuit model
2
4
6
3
5
7
1
x5
x6
x3
x4
x1
x2
2
4
6
3
5
7
1
2
4
6
3
5
7
1
layers:
1
2
3
input
User gives input bits
Programmer specifies layer: gates to go in each row
Computation flows from inputs to layers 123…
Notes: So the programmer defines a circuit by specifying a layer: the gates that go in each row.
The user gives n input bits to the first layer, n=6 here.
And the layers repeat forever, with computation flowing from left to right.

## Slide 13: Scooped?

## Slide 14: Example circuits with same gate in every row
1
1
0
0
1
1
1
1
0
0
1
1
Copy
i1
i2
i1
i2
i1 | i2 | o1 | o2
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 1 | 1
0
0
0
1
1
1
1
1
1
0
0
0
Sorting
i1 | i2 | o1 | o2
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 1
i1
i2
OR(i1,i2)
AND(i1,i2)
Copy gates
Sorting gates
Notes: Let’s go through some more examples.
The simplest circuit we could imagine is copying: every gate is simply the identity function, so the 1’s and 0’s move in a straight horizontal path to the right.
From now on I’ll draw circuit evaluations like this, with an asterisk indicating a 1, and everywhere else is 0’s.
We already saw how to sort: pushing the 1’s up to the top as computation flows from left to right.

## Slide 15: Example circuits with different gates in each row
1
0
0
1
0
1
00
0
1
00
Parity
MultipleOf3
1
1
1
0
1
1
0110112
= 5910 = 3∙19 + 2
1110112
1
0
1
1
0
1
00
0
0
00
0
1
1
0
1
1
= 2710 = 3∙9
Notes: Let’s go through some more examples.
The simplest circuit we could imagine is copying: every gate is simply the identity function, so the 1’s and 0’s move in a straight horizontal path to the right.
From now on I’ll draw circuit evaluations like this, with an asterisk indicating a 1, and everywhere else is 0’s.
We already saw how to sort: pushing the 1’s up to the top as computation flows from left to right.

## Slide 16: Randomization: “Lazy” sorting
0
0
0
1
1
1
1
1
1
0
0
0
2
4
6
3
5
1
7
copy gate
sort gate
If 1 and 0 out of order, flip a coin to decide whether to swap them.
0
0
0
1
1
1
1
1
1
0
0
0
Notes: Here’s a simple example of a randomized circuit: we call this lazy sorting.
Every row has a copy and a sort gate, which get randomly chosen.
So the bits eventually get sorted, but it takes longer than normal sorting,
because sometimes copy is chosen when a 1 and 0 should be swapped.

## Slide 17: Deterministic circuits
answer yes/no question
simulate cellular automata
Rule110
time
Theorem: Rule 110 can efficiently execute any algorithm.
[Neary, Woods, ICALP 2006]
[Cook, Complex Systems 2004]
“count” as high as possible
Parity
MultipleOf3
Palindrome
Cycle63
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 1 | 2
yes
no
Notes: We saw how to compute parity, which makes a stripe of 1’s, or not, depending on whether the initial number of 1’s is odd.
Erik Winfree found a circuit to decide if the bits are a palindrome, meaning they read the same forward and backward, like the name of this Swedish band, making this pattern if so, and this other pattern if not.
The bits could represent an integer in binary, and we want to know if it’s a multiple of 3.
  These bits are the binary expansion of 21, a multiple of 3, and the circuit makes this pattern.
  Let’s flip the first bit to a 1, quick: what’s that binary integer? Is it a multiple of 3? … turns out no, it’s not, so this other pattern appears
These are all examples of what computer scientists call decision problems, questions with a yes/no answer.
Each layer receives 6 bits as input, so after 2^6 = 64 layers, the circuit must repeat…
can we design a circuit that goes through all 64 strings before repeating?
In order words, how high can these circuits count?
We still don’t know, but Erik found this one that goes through 63 strings before repeating.
Another model of computation similar to ours is a cellular automaton, which examines triples of bits and updates the middle one based on all three.
  This one is called “Rule 110”, which makes this pattern.
  Our model can only look at pairs, not triples, so it’s not obvious if it could emulate the behavior of Rule 110.
  In fact, there are some cellular automata that our model provably cannot emulate, but Damien figured out how to do Rule 110.
  Rule 110 is especially interesting to computer scientists because of this theorem, which Damien helped to prove a decade ago, stating that with enough bits, Rule 110 can efficiently execute any algorithm whatsoever.

## Slide 18: Randomized circuits
use biased coin to simulate unbiased coin
Pr
= Pr
= ½
for any (positive) probabilities for the randomized gate
LazyParity
RandomWalkingBit
DiamondsAreForever
FairCoin
Notes: Here’s some more examples of randomized circuits.
We saw lazy sorting; lazy parity is similar, bring 1’s slowly to the middle and cancel them in pairs when they meet.
Random walking bit just has a single bit that walks up and down randomly.
Here’s one of Damien’s favorites: usually it’s all 0’s, but occasionally a pair of 1’s materialize in the middle, move out to the edges and back, and annihilate each other, making diamonds, forever.
This is my favorite randomized circuit.
It has one gate with two randomized choices, and it results in one of two eventual patterns: all 0’s eventually, or stripes of 1’s near the bottom.
Each pattern appears with probability exactly ½.
  Here’s the cool part: this happens no matter what are the underlying randomized gate probabilities:
  they could be 99 to 1, and you’ll still get half the circuits with stripes, and the other half without, using a technique called von Neumann rejection sampling.

## Slide 19
100 nm
Notes: So we have all these circuits that we thought up, and here’s images of them being simulated.
What else did we do?
We went in the lab, and
  using self-assembling DNA strands,
  we implemented every one of these circuits,
  and many more,
  and they all worked,
  with very low error rates.
The scale bar on top tells you how big this stuff is, BUT, you’re not yet supposed to understand what… this… stuff… actually is.
That’s what the rest of the talk is about.

## Slide 20: Hierarchy of abstractions
Bits: Boolean circuits compute
Tiles: Tile self-assembly implements circuits
DNA: DNA strands implement tiles
Notes: We’ll move now from static circuits,
which lay still while bits flow through them,
to an abstract model of self-assembling square tiles,
which dynamically bind to each other.
The third part of the talk shows how to actually build these tiles from DNA.

## Slide 21: Gates  Tiles
1. Compile gates to tiles
i1
o1
i2
r
gate
o2
tiles
(4 per gate)
Ur
1r
1r-1
0r
Ur
0r-1
1r
Ur
0r-1
0r
i1 | i2 | o1 | o2
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
Each entry of a gate’s truth table is encoded by a tile
Ur
1r-1
0r
1r
0r
Each glue encodes a bit and a row
0r
0r-1
1r-1
1r-1
0r-1
Notes: Each gate is represented by four tiles.
Each entry of the gate’s truth table corresponds to a tile.
Each side of the tile has a glue, which helps it bind to other tiles.
Each glue encodes two pieces of information:
  a bit, and
  the gate’s row, so a 0 on row 2 will have a different glue than a 0 on row 3
The input bits to the gate are on the left of the tile and the output bits are on the right.

## Slide 22: How tiles compute while growing (algorithmic self-assembly)
U3
02
03
U3
12
03
U3
02
13
U3
12
13
13
02
two glues match: cooperative binding
U2
U3
U4
U5
U6
U_
U_
U1
U7
2
4
6
3
5
7
1
2
4
6
3
5
7
1
2
4
6
3
5
7
1
x1
x2
x3
x4
x5
x6
x1
x2
x3
x4
x5
x6
_
_
U2
U3
U4
U5
U6
U_
U_
U1
U7
U2
U3
U4
U5
U6
U_
U_
U1
U7
one mismatch
two mismatches
“data-free” tile wraps top to bottom to form a tube
U_
12
03
03
03
12
12
13
02
U_
U_
U_
U_
U_
U_
U_
U_
U_
U1
U1
U1
U1
U1
U1
U1
U1
U1
U1
U2
U7
U2
U7
U7
U2
U2
U2
U2
U2
U2
U2
U7
Notes: Now we’ll see how tiles can self-assemble so as to carry out the circuit computation.
We start with glues representing the input bits somehow just hanging there in space; in the next part of the talk we’ll see how to implement this.
Tiles attach to these glues, and to each other, in an order like this.
For now I’m hiding the glue information just to show how tiles grow.
Now, I’m drawing the tiles as if they lay flat, but in fact, there’s one special tile that carries no “data” (its glues encode a row but no bit),
and it helps wrap the tiles around into a tube.
To help you visualize, I’ve used advanced GPU hardware to create this 3-dimensional rendering of tiles rolled into a tube.
So the tiles grow a tube from left to right.
Now let’s see some actual glue information… suppose these two tiles have glues encoding bits 0 and 1.
There’s four tiles that could go in row 3, one for each pair of input bits.
But two of these tiles mismatch one of those glues.
One of the tiles mismatches both of the glues.
Only 1 of the 4 tiles correctly matches both of the glues, so it will be the only one to bind here.
We call this cooperative binding, since both glues must cooperate to attach the tile.
And of course, this tile has two other glues on the right side, which are the outputs of the gate on this input.
This is how a tile attaching can compute its gate’s function.

## Slide 23: Hierarchy of abstractions
Bits: Boolean circuits compute
Tiles: Tile self-assembly implements circuits
DNA: DNA strands implement tiles
Notes: Finally, we build the tiles, out of our favorite molecule.

## Slide 24: Structural DNA nanotechnology
a.k.a. DNA carpentry

## Slide 25: DNA as a building material
=
TCGGAAATAAAATCGGAC
AGCCTTTATTTTAGCCTG
TAGCGTAATT
ATCGCATTAA
=
DNA strands can bind even if only part of strands are complementary:

## Slide 26: DNA origami
scaffold DNA strand
staple DNA strands
folded DNA origami
heat to 90C, cool to 20C over an hour
(M13mp18 bacteriophage virus)
© http://openwetware.org/wiki/Biomod/2014/Design
© Shawn Douglas
Paul Rothemund
Folding DNA to create nanoscale shapes and patterns
Nature 2006
(+ water + salt)

## Slide 27: DNA origami
Paul Rothemund
Folding DNA to create nanoscale shapes and patterns
Nature 2006
Atomic force microscope images
100 nm

## Slide 28: DNA nanotechnology applications
DNA origami opens to deliver antibody only in presence of two protein antigens
41t-specific latch
TE17-specific latch
Shawn Douglas, Ido Bachelet, George Church, A logic-gated nanorobot for targeted transport of molecular payloads, Science 2012
open
antibody Fab’ fragments
nanoscale resolution surface placement
X-ray crystallization scaffolding
molecular motors
super-resolution imaging
molecular circuits
biological:
smart drugs
mRNA detection
cell surface marker detection
genetically encoded structures
example
art
Ashwin Gopinath, Evan Miyazono, Andrei Faraon, Paul Rothemund, Engineering and mapping nanocavity emission via precision placement of DNA origami, Nature 2016
nonbiological:
Grigory Tikhomirov, Philip Petersen, and Lulu Qian. Fractal assembly of micrometre-scale DNA origami arrays with arbitrary patterns. Nature 2017.

## Slide 29: Other applications of DNA nanotechnology
4 μm wide scan
zoom in

## Slide 30: Cherry-picked samples
Beth Yim
100 nm
Notes: Two of the patterns were apparent to my girlfriend, Beth Yim, because they spelled her name.
I’m sorry, did I say “girlfriend” just now? I must have misspoken, I meant to say “fiancé”.
I led her into every woman’s dream romantic venue, this windowless, phosphorescent white room where Damien Woods keeps his AFM, and that’s where I showed her 100 billion marriage proposals.
And after some accelerated training that wasn’t entirely within the safety rules of the lab, she was able to mix staples to give 100 billion replies.

## Slide 31: DNA single-stranded tiles
glue 4
glue 3
glue 2
glue 1
assembly
Yin, Hariadi, Sahu, Choi, Park, LaBean, Reif
Programming DNA tube circumferences
Science 321, 824-826 (2008)
Notes: There’s many DNA motifs for creating self-assembling tiles.
We use the single-stranded tile, which is just a single strand of DNA, logically sectioned into 4 binding domains, each implementing a glue.
So the tile isn’t shaped like a square, but it binds to 4 neighboring tiles in a so-called square lattice.
This slide shows the tiles in a flat ribbon shape, but…

## Slide 32: Single-stranded tiles for making any shape
Bryan Wei, Mingjie Dai, and Peng Yin. Complex shapes self-assembled from single-stranded DNA tiles. Nature 2012.

## Slide 33: Uniquely addressed self-assembly versus algorithmic
single DNA origami
uniquely-addressed tiles
staple strand for position (4,2)
tile for position (4,2)
origami for position (4,2)
Unique addressing: each DNA “monomer” appears exactly once in final structure:
array of many DNA origamis
Algorithmic: DNA tiles are reused throughout the structure.

## Slide 34: Single-stranded tile tubes
Yin, Hariadi, Sahu, Choi, Park, LaBean, Reif, Programming DNA tube circumferences, Science 321, 824-826 (2008)
DNA-level diagram of 20-helix tube
Notes: We’ll actually construct tiles to wrap into a 16-helix tube.
So there’s no special tiles for the “top” or “bottom”; they’re all symmetric.

## Slide 35: Tubes and ribbons
remove “seam” by strand displacement
500 nm
AFM image
tube
ribbon
Notes: So we grow tiles into tubes, and we could image those with an atomic force microscope.
But we’d like to see more detail on individual helices, so we do the following.
We pick out one helix and rip it open using strand displacement.
Then, by laying the tiles down on mica, they flatten into a ribbon.

## Slide 36: Seeded growth
DNA origami seed
single-stranded tiles implementing circuit gates
15
04
15
14
13
02
03
02
13
12
03
12
05
04
05
14
05
14
15
04
biotins if output = 1
barrier to nucleation (tile growth without seed) at [tile]=100 nM and
temperature=50.9° C
single-stranded “input-adapter” extensions encoding 6 input bits
can later add streptavidin to bind biotins and visualize where the 1’s are
hold 8-48 hours
seed
input-adapters
growing tiles
Notes: We’ll operate at a concentration and temperature at which the tiles actually won’t prefer to grow on their own, there’s an energetic barrier to nucleation.
But, by adding a seed structure, the tiles grow from the seed.
Our seed is a DNA origami rectangle, rolled up into a tube.
It has single-stranded extensions we call “adapters” to which the tiles bind to initiate growth.
By choice of DNA sequence for these adapters to encode 0 or 1 glues, they supply the 6-bit input to the circuit.
We add the tiles, 100 of them to implement a particular circuit (I’m just showing 5 here).
So the tiles encode the circuit, the origami seed encodes the input through its adapters, and the tiles grow from the seed to carry out the circuit computation.
We’d like to know which tiles end up where, but that level of detail is difficult to read out.
What we can do, is put a biotin on any tile with a 1 output, so by later adding streptavidin, we can at least see where are the 1’s in the circuit.

## Slide 37: DNA sequence design
✓
Random sequences vs designed sequences
energy (-kcal/mol)
4
6
8
10
12
14
16
18
energy (-kcal/mol)
4
6
8
10
12
14
16
18
0.9
0.5
0.0
normalized count
0.9
0.5
0.0
normalized count
0
0
0
0
incorrect binding
more favorable
2 bonds
1 bond
Other goals:
low strand secondary structure
low interaction between strands
0
1
1
0
correct binding
✓
2 bonds
1 bond

## Slide 38: Bar-coding origami seed for imaging multiple samples at once
label with
streptavidin
Generate plate map
some staples of origami seed have version with a biotin
represents some combination of circuit and input, e.g.,
013 = “parity circuit, input=011010”
Notes: We want to run several experiments in parallel and mix them together in one imaging session, since anyone who’s used an AFM knows they can be cranky, so once it works we’d like to get a lot of data at once.
Now, functionally the origami without the adapter strands always acts the same, it’s just rectangle rolled up into a tube.
But, to help us tell different experiments apart in a single imaging session, we mark each origami with some experiment-specific information.
How do we do this? Some of the origami staples have a version with a biotin.
By selecting an appropriate subset of these
and then adding streptavidin, we can spell a 3-digit sequence of our choosing on the unrolled origami rectangle, which represents both the circuit and the input to the circuit in that experiment.

## Slide 39: Experimental protocol
Mix
To execute circuit on input :
15
04
15
14
13
02
03
02
13
12
03
12
05
04
05
14
05
14
15
04
  origami (bar-coded to identify both and )
  “adapter” strands encoding
  tiles computing
Anneal 90° C to 50.9° C in 1 hour (origami seeds form)
Hold at 50.9° C for 1-2 days (tiles grow tubes from seed)
Add “unzipper” strands (remove seam to convert tube to ribbon)
Add “guard” strands (complements of output sticky ends, to deactivate tiles)
Deposit on mica, buffer wash, add streptavidin, AFM
Notes: Here’s the full experimental procedure. To execute a circuit on input bits x: mix together the
origami, bar-coded to identify both and x
adapter strands to encode the input x
the appropriate hundred tiles implementing the circuit
anneal slowly from 90C to about 50C, this lets the origami seeds assemble
hold there for a while, which lets the tiles grow onto the seeds
then there’s a bunch of important steps I don’t have time to explain,
and then we image.
Here’s the full experimental procedure. To execute a circuit 𝛾 on input bits x: mix together the
origami (bar-coded to identify both γ and x, but otherwise functionally the same in every experiment)
adapter strands to bind to the origami, whose extending sticky ends encode the input x
the appropriate hundred tiles representing the circuit γ
anneal slowly from 90C to about 50C, this lets the origami seeds assemble
hold there for a while, which lets the tiles grow onto the seeds
then there’s a bunch of important steps I don’t have time to explain,
and then we image.

## Slide 40: Results
def test_parity():
actual = parity('100101')
expected =
assertEquals(expected, actual)
Notes: Now lets look at the results.
What do we expect to see?
  An origami rectangle, with 3 digits written on it.
  You’ll have to take my word that the 3 digits always represent the proper experiment.
  and streptavidins to the right of there, showing how the 1’s moved around as the circuit grew.

## Slide 41
100 nm
Sorting
Parity
MultipleOf3
Palindrome
Recognise21
Zig-Zag
Copy
Notes: Our first circuit was sorting. As we scan from left to right, we should see the 1’s move from the bottom to the top, and we do.
Lazy sorting is similar… it takes longer for the 1’s to reach the top, but they get there.
This shows 3 different runs of lazy sorting on the same input, showing that while the 1’s always get to the top, unlike normal sorting, they don’t do it the same way every time.
Rule 110 on 6 bits doesn’t do much interesting, but it does it very well.
And here are the palindrome circuit and the multiple-of-3 circuit.

## Slide 42
RandomWalkingBit
LazyParity
LeaderElection
AbsorbingRandomWalkingBit
LazySorting
Waves
Notes: Here’s parity, recall
  a stripe of 1’s should appear if the initial number of 1’s is odd,
  eventually all 0’s otherwise.
Lazy parity does the same thing, only slower.
This is the circuit that counts 63 bitstrings before repeating; as you can see, reading this one is a little tougher.
Waves is an interesting randomized circuit I didn’t show yet: this has a stripe of 1’s along the bottom, but occasionally at random the 1 CRESTS to the top before crashing back down.
Most circuits were tested on only a handful of inputs…

## Slide 43
Rule110
FairCoin

## Slide 44: Counting to 63
Is there a 64-counter?
1 2 3 …
…62 63 1 2 3 …
Circuit with 63 distinct strings
42
No!
Proof by Tristan Stérin, ENS Lyon & Inria
(Consequence of following theorem: Any bijective Boolean circuit having one output bit that does not depend on all of its input bits cannot compute odd bijections.)

## Slide 45: Parity tested on all inputs
σ(6-bit input) = 3-digit barcode representing that input
32 inputs with even # of 1’s
32 inputs with odd # of 1’s
26 = 64 inputs with 6 bits
150 nm
We used all 355 tiles in some experiment, so we’ve verified “all tiles work”.
For 14 circuits, every tile for that circuit was used for some input, verifying all gate tiles work “together”.
Notes: Parity we tested on all 64 inputs.
32 of them have an even number of 1’s, so we expect no stripe, that’s what you see on the left
The other 32 we expect a stripe of 1’s; that’s on the right.
This is one way to do a so-called “full coverage test”, but we can imagine others:
  All 356 of the tiles in our library were used in some experiment, so we’ve verified that in some sense “all tiles work”
  For 14 of the circuits, although we didn’t test every input, we tested enough inputs that every tile in that circuit got used for some input, so we’ve verified for those that all gate tiles work “together”.
Now, the images I’ve shown so far are obviously cherry-picked, so next let’s see some raw data.

## Slide 46
500 nm
12 μm AFM image of parity ribbons for several inputs whose output is 1
error statistics:
seeding fraction: 61% of origami seeds have tile growth into a tube
error rate: 0.03% ± 0.0008 per tile attachment
(1,419 observed errors out of an estimated 4,600,351 tile attachments, comparable to best previous algorithmic self-assembly experiments)
Notes: This is a 12 micron AFM image showing parity on several inputs whose answer is 1.
Zooming in, we expect to see stripes of streptavidins on each ribbon, and we do.
Let’s look at some non-ideal parts of this image.
Here’s a tile attachment error: there is a stripe on this ribbon for a while, and then it disappears, erroneously flipping a 1 into a 0.
Here are ribbons with no origamis attached.
We believe from control experiments that these did not grow on their own, that they were ripped away from origamis, but of course we don’t know for sure.
And finally, the most frustrating and frequent type of error, which we tried several ideas to eliminate but never could:
Several origami seeds have little or no growth of tiles;
There appears to be some energetic barrier to initiating growth.
Now, the numbers I’ll throw up here are very approximate, very back of the envelope, we are still in the process of counting and analyzing data, but these are roughly accurate.
About ½ of origami seeds have significant tile growth into a tube.
Of those, 92% have no bit-flipping error, in other words, the circuit computation is correct.
Now, that looks like an 8% error rate, but bear in mind this is the error rate per tube.
Most tubes are hundreds of nanometers long, corresponding to hundreds to over a thousand tile attachments,
so this implies an error rate per tile attachment of something like 1/10,000,
comparable with the best prior algorithmic self-assembly experiments,
but now demonstrated on a much wider variety of computations.

## Slide 47: What did we learn?
A small(ish) library of molecules can be reprogrammed to self-assemble reliably into many complex patterns, by processing information as they grow.
more algorithmic control
than periodic self-assembly
single-stranded tile tubes (Yin et al., Science 2008)
double-crossover tile lattices (Winfree et al., Nature 1998)
order of magnitude more tile types available than previous
algorithmic self-assembly
(Rothemund et al., PLoS Bio 2004)
double-crossover tile lattices
(Fujibayashi et al., Nano Letters 2008)
(Barish et al., PNAS 2009)
(Evans, Ph.D. thesis 2014)
fewer types of DNA strands required than uniquely-addressed self-assembly
DNA origami (Rothemund, Nature 2006)
single-stranded tile lattice (Wei et al., Nature 2012)
Contrasting with other self-assembly work:
Notes: So what did we learn?
A single library consisting of a relatively small number of different types of molecules can be mixed and matched to construct a huge variety of complex patterns by processing information as they grow, and this can be done reliably.
Contrasting with other self-assembly approaches:
Compared to “periodic” approaches such as 2D unbounded lattices or periodic tubes, we have greater control over the sort of pattern formed. (Although we aren’t controlling the underlying structure. As in previous work, it’s an unboundedly growing tube.)
Compared to “uniquely-addressed” or “hard-coded” approaches such as DNA origami or single-stranded tile lattices, we require fewer distinct types of molecular components that must be synthesized. (On the other hand, we need to design those strands more carefully, since our system is more sensitive to energetics.)
Compared to previous algorithmic self-assembly, which used tiles with shorter sticky ends, we have available more types of tiles, in order to achieve a greater variety of computations.

## Slide 48: Next big challenge: Algorithmically control shape
We “drew” interesting patterns on a boring shape (infinite rectangle)
Can we grow interesting shapes?
σsmiley_face
σdolphin
Theorem: There is a single set T of tile types, so that, for any finite shape S, from an appropriately chosen seed σS “encoding” S, T self-assembles S.
[Complexity of Self-Assembled Shapes. Soloveichik and Winfree, SIAM Journal on Computing 2007]
These tiles are universally programmable for building any shape.
?
?

## Slide 49: Thank you!